## Slide 1: Thermistor Calibration

## Slide 2: DISCLAIMER & USAGE
The content of this presentation is for informational purposes only and is intended for students attending Louisiana Tech University only.
The authors of this information do not make any claims as to the validity or accuracy of the information or methods presented.
Any procedures demonstrated here are potentially dangerous and could result in damage and injury.
Louisiana Tech University, its officers, employees, agents and volunteers, are not liable or responsible for any injuries, illness, damage or losses which may result from your using the materials or ideas, or from your performing the experiments or procedures depicted in this presentation.
The Living with the Lab logos should remain attached to each slide, and the work should be attributed to Louisiana Tech University.
If you do not agree, then please do not view this content.
boosting application-focused learning through student ownership of learning platforms

## Slide 3: What is a temperature?
Sense of warmness of coldness of a material
Measure of the average thermal energy of particles in a material
Thermodynamic property of a substance that is related to the average energy of microscopic motions in a substance.

## Slide 4: Measuring Temperature with a Thermistor
Measures electrical resistance changes with temperature
  As resistance decreases, temperature increases
Advantages
  High Output
  Fast
  Two-wire Ohm Measurement
Disadvantages
  Non-linear
  Limited Temperature Range
  Fragile
  Current Source Required
  Self-heating
Circuit Diagram Symbol:

## Slide 5: Measure Thermistor Resistance
Connect a thermistor to your multimeter
Measure its resistance
Hold the thermistor to change the temperature
Measure its resistance
What do you observe?
Resistance Decreases as Temperature Increases

## Slide 6: Collect Data Using Arduino
Connect the thermistor to your breadboard and Arduino
Use the given sketch to print analog values read by the voltage divider circuit
5V
analog input 5
thermistor
10kW
int val = 0;
void setup() {
Serial.begin(9600);
}
void loop() {
val = analogRead(5);
Serial.println(val);
}
Press your fingers over the thermistor (Increase temperature).
What do you observe?
Analog Value Increases as Temperature Increases

## Slide 7: Collect Data Using Arduino
Analog values can be converted to voltage drop across the 10kΩ resistor
5V
analog input 5
thermistor
10kW
Recall Resistors in series and Ohm’s Law:
  If the voltage drop across the 10kΩ resistor increases, then the voltage drop across the thermistor .
  If the voltage drop across the thermistor decreases, then the resistance of the thermistor
  .
Summary: An increases in analog values read by the Arduino means the resistance of the thermistor is which means temperature is increasing.
Is this consistent with the values read by your multimeter at the beginning of class?
decreases
decreases
decreasing

## Slide 8: Calibration Equation
Develop an equation that correlates analog values to temperature values
  Use known temperature values that are mapped to analog values read by the Arduino
Setup per three students:
  1 Cup
  1 digital thermometer
Setup per Individual
  Waterproofed thermistor in voltage divider circuit
  Arduino, laptop, Excel
This is an individual activity. Share the cups and thermometer but perform the calibration on your own.
Procedure (Details on subsequent slides):
  Step 1: Waterproof your thermistor.
  Step 2: Fill your cup with one of the water temperatures (cold, warm, or hot).
  Step 3: Write down the °C value of the water from the thermometer and its corresponding analog value from the serial monitor.
  Step 4: Repeat steps 2 and 3 for the all water temperatures. You should have a total of three data points (a °C value and analog value for each cup).
  Step 5: Record data points in Excel & plot the data points on a scatter plot.
  Step 6: Add the appropriate trendline and obtain the corresponding equation.

## Slide 9: Step 1: Waterproofing Thermistor
Clip approx. 1/2in off of thermistor legs
Attach wire extensions to each leg
Cut heat shrink material to approx. 3in and slide it over the thermistor
Note: Leave approx. 1/2in of material passed the thermistor to be used as for a seal
Shrink material using heat gun
Clamp end of heated material to seal in the thermistor
Be sure to not crush the thermistor when clamping material
Strip wires jumper wires and connect them to wire extensions
1/2in of extra material
Tip of Thermistor here
Heat the end last so that it is amenable when clamping

## Slide 10: Step 2: Fill cup about 2/3 full with cool, warm, or hot water
Use sinks in the room to fill a cup with either cool water, warm water and hot water.
Step 3: Collect °C and analog values for each cup of water
Insert thermometer and thermistor into water while running the sketch that prints analogRead values.
Wait until values from thermistor circuit reach a steady value.
Record the temperature from the thermometer and the analog value on the Serial Monitor.
Repeat for each cup of water (three data points, °C value and analog value for each cup).
Return cups and thermometers when everyone is finished collecting data.
Step 4: Repeat Steps 2 & 3 for all water temperatures.
cold
warm
hot

## Slide 11: Step 5: Record data points in Excel and Plot data points Step 6: Add trendline and equation on chart
Temperature | Analog Value
ᵒC | 0 to 1023
12.2 | 384
22.1 | 484
57.4 | 782
Chart: Analog Value versus Temperature
| 12.2 | 22.1 | 57.4
Calibration | 384 | 484 | 782
Calibration Equation:
use five digits for these fitting constants

## Slide 12: Using the Calibration Equation
When temperature is known, input temperature and get corresponding analog value
What if temperature is not known?
Invert Equation
Algebraically: Solve for Temperature
Graphically: Swap x and y axis
Chart: Temperature versus Analog Value
| 384 | 484 | 782
t | 12.2 | 22.1 | 57.4
Small but negligible difference in equations depending on method used

## Slide 13: Using the Calibration Equation
Adapt the Arduino sketch to print the values of temperature
  Use Excel or your calculator to check the equation
    Tip: Set the analog value to be a constant while checking
  What happens when you declare the temperature variable to be a float instead of an int
    float is a data type that allows for decimal values
Adapt the sketch to print both the analog value and its corresponding temperature value as a decimal